Requirements USB-Controller

- have to be solderable
- Driver for Linux
- Data transfer rate: USB-Controller 2.0 Highspeed with 480 MBit/s
- ULPI compatible
- Quantity of I/O-Pins

Calculate data transfer rate for one Kinect:
USB 2.0 Highspeed !netto! data transfer rate:
35MB/s - 40MB/s

Kinect data transfer rate:
www.openkinect.org/wiki/faq:
Resolution 640 x 480:
Depth camera:	12 MB/s
Color camera:	9 MB/s

Comparison of USB-Controller

Requirements		ISP 1362	ISP 1761	SAF 1761

Date of production		~ 2004	x	2015
Solderable		yes	yes	yes
Driver for Linux		yes	yes	yes
Data transfer rate		96 Mbit/s	480 Mbit/s	480 Mbit/s
ULPI compatible
Quantity of I/O Pins		27Pins max	16Bit: 41Pins ; 32Bit: 57	16Bit: 41Pins ; 32Bit: 57