Kinect and USB-Controller Documentation
Initial Situation
The customer wants two Kinects to be put on the X-Copter. They are to provide 3D-Image data to map the surrounding locale of the X-Copter. To be able to communicate with two Kinects, two USB- Controllers are needed. This is because one Kinect needs at least ~21 MB/s data transfer rate for 3D-Images at 640×480 pixels with 30 frames per second, which is too much for one controller to handle. 21 MB/s are divided into ~12MB/s for depth camera and 9 MB/s for color camera [1]. For proper 3D-Image data color- and depth camera have to work at the same time and can not be separated, which strikes out the option to save bandwidth with using only one camera at the time.
Kinect cameras will be connected via USB 2.0 plug to the USB-Controllers. For the Controllers to be able to communicate with the DE1-SOC system, an interface has to be implemented into the existing SOPC for communication between the devices. Real time 3D-Data processing will be the task of another external system with an Intel processor. Our customer stated that on a similar side project of him even an Intel I7 quad core processor is struggling with processing the data. For further information about hardware requirements of Kinect-Systems refer to [2].
Requirements for the USB-Controller
There are certain cut in stone requirements for the USB-Controller to work with Kinect and to fit in the design of our system:
- Must be available on the market
- Must not exceed the quantity of pins our system is able to offer
- Drivers for Linux have to be available
- Chip has to have outgoing pins to be solderable
- Full High-Speed data transfer rate of 480 MBit/s
- (Should be ULPI compatible if present Waveshare 3300-Transceivers are meant to be used)
Common USB-Controller Packages
There are three different common USB-Controller Packages that are solderable with the equipment available: QFN (Quad Flat No-leads package), LQFP (Low Profile Quad Flat Package) and TQFP (Thin Quad Flat Package). Information, advantages and disadvantages of these packages can be reviewed at [5]. QFN is harder to solder which is why QFP style packages are the preferred choice.
Comparison of USB-Controllers
Chips with packages that are not solderable with the equipment at our disposal will not go into the equation.
	ISP1362BD	ISP1761BE	SAF1761BE [3]	FT313H(L/P) [4]
Date of production	Rev. 04 / 12.2004	Rev. 01 / 01.2005	Rev.02 / 06.2012	Ver.1.2 / 2013
Package	LQFP64	LQFP128	LQFP128	64 LQFP / 64 TQFP
Driver for Linux	yes	yes	yes	yes
Transfer rate	96 Mbit/	480 Mbit/s	480 Mbit/s	480 Mbit/s
RAM Memory	unkn.	unkn.	unkn.	48 KB
ULPI compatible	unkn.	unkn.	unkn.	unkn.
Quantity of I/O Pins	27 Pins	16Bit: 41 Pins / 32Bit: 57 Pins	16Bit: 41Pins / 32Bit: 57 Pins	?
Info	Discontinued	Discontinued	Available	Available
Pros	+ Frank Seifert implemented this chip in his bachelor project	+ speed / + similar to ISP1362BD	+ speed / + similar to ISP1761BE	+ speed / + 64 PIN package / + UMFT313EV Development Module available
Cons	- speed (too low for Kinect) / - not available	- not available	- used mainly in automotive projects / - no evaluation board	Unkn. As of time of writing

Sources:
1. http://openkinect.org/wiki/FAQ
2. https://msdn.microsoft.com/en-us/library/jj131032.aspx
3. http://www.nxp.com/products/automotive/multimedia/usb/SAF1761BE.html
4. http://www.ftdichip.com/Products/ICs/FT313H.html
5. http://en.wikipedia.org/wiki/Quad_Flat_Package
Pictures:
1. http://www.cypress.com/?id=167